## Slide 1
GOOD PRACTICES TRAINING FOR
CUTTING, GRINDING AND SANDING

## Slide 2
PREAMBLE (FOR TRAINER)
As part of the education step in implementing the NEPSI Good Practices, NEPSI has developed a set of educational resources.
Each PowerPoint Training pack covers a topic relevant for workers across all industries that use materials containing crystalline silica. The packs provide information about the dust exposure risks related to the topic and the good practices and measures available to reduce them. The purpose of the training is to inform and educate workers to help them to use the control measures effectively and reduce their exposure to respirable crystalline silica (RCS) in the workplace.
Use the blank template and placeholders to add additional information to this training pack as needed.

## Slide 3
PLEASE NOTE
The information in this PowerPoint training is advisory in nature and informational in content. It is not a standard or regulation, and it neither creates new legal obligations nor alters existing obligations created by health legislation and policy.

## Slide 4
INTRODUCTION
Learning to protect yourself against work-related hazards is a priority.
In this PowerPoint training, you will learn about:
Health risks related to high-energy industrial processes, that may cause exposure to harmful respirable crystalline silica dust (RCS)
Good practices to apply when cutting, grinding and sanding
Text for trainer to fill – if you’ve added a custom slide, insert a brief overview of the contextual material
Notes: Excessive exposure to respirable crystalline silica (RCS) can lead to serious health problems for workers in the long-term. For that reason, it is important that all workers are aware of the good practices that limit or eliminate exposure to silica dust.
This training provides guidance for cutting, grinding and sanding materials containing crystalline silica.

## Slide 5
DUST CONTROL TECHNIQUES
Cutting, grinding and sanding processes can be controlled using the five main dust control techniques.
GOOD HYGIENE / HOUSEKEEPING
Washing work clothes and vacuuming up dust produced by processes stops dust accumulating over time – a clean workspace is a safe one
ENCLOSURE
Conducting RCS producing processes in a sealed environment prevents dust exposure at the source
EXTRACTION / VENTILATION
Capturing RCS at source, before we are exposed to it, and replacing contaminated air with clean air.
PROTECTIVE EQUIPMENT
PPE (e.g. Face masks) protects workers from dust when all other control measure are insufficient to control exposure risks
WATER
Keeping processes wet prevents dust becoming airborne by capturing particles with water

## Slide 6
THE RISKS FROM THIS ACTIVITY
This activity can be very dusty
Long term exposure to high levels of RCS can cause disabling lung disease
It’s important that we protect ourselves from exposure to this airborne dust every day.
By following good practices today, we protect our health for the future.
How will you spend your retirement?
Notes: Bag emptying processes and improper handling of the empty bags can lead to significant levels of dust exposure. For this reason, good practices related to bag emptying must be followed. The use of automatic or semi-automatic bag dumping stations is recommended for emptying small bags.

## Slide 7
HOW HIGH-ENERGY PROCESSES GENERATE RCS
Cutting, grinding and sanding are high-energy processes, which can generate a lot of dust when applied to certain materials:
The dust generated from many industrial materials (e.g. sandstone) is hazardous; control measures are necessary to reduce dust exposure.
The dust generated may contain respirable crystalline silica (RCS), which when inhaled over extended periods of time can cause silicosis.

## Slide 8
TOOLS THAT GENERATE DUST
Angle grinders
Angle cutters
Cut-off machines
Electric wall chasers
Drilling machines
Notes: Cutting, grinding and sanding are high-energy processes that can create hazardous amounts of dust.

## Slide 9
BEFORE CUTTING, GRINDING AND SANDING
Make sure the area is well-ventilated
Check the equipment for signs of damage
If using an extraction system, make sure it’s functioning properly
Clean slabs and machines with running water
Notes: There are several safety precautions to take before starting high-energy processes to reduce dust exposure and unnecessary injury.

## Slide 10
DURING CUTTING, GRINDING AND SANDING
If using wet processes, check that the water supply is adequate
Always use respiratory protection for dust-intensive activities
Use of water-integrated machinery and tools significantly reduces the level of silica dust.
When possible, keep machine safety doors closed
Use Local Exhaust Ventilation (LEV) to capture silica dust at the source and transport it away from the employee's breathing area
Text for trainer — Add additional text about measures related to cutting, grinding and sanding relevant to your own context
Notes: Wet processes help reduce dust exposure by capturing airborne dust with water. If the device is adapted for water injection, wet processes are recommended. Dry fabrication generates very high levels of Silica Dust – don’t use dry tools!
PPE should be worn as indicated by signage and pictogram. For dust-intensive activities, always use a respiratory protection.

## Slide 11
DOS AND DON’TS OF CUTTING, GRINDING AND SANDING
DO
Use a dust extraction system when available
Take advantage of ventilation systems when working in enclosed spaces
Use water-integrated tools to keep the dust down
Use PPE in indicated areas
DON’T
Use equipment that is faulty or damaged
Let dust extraction bins overflow
Use devices in combination with inappropriate processes and equipment (e.g. wet processes with a device that doesn’t support water infiltration)

## Slide 12
EMPTY SLIDE
Use this slide to create custom training material specific to a work environment/context
To change the image, right click > change picture > from file
To create more slides, click the ‘New Slide’ tab above
Notes: *Note for trainer* Consider adding additional information specific to your own working context.

## Slide 13
CONCLUSION
Cutting, grinding and sanding are high-energy processes, which generate a lot of dust.
Remember:
Make sure the enclosure is well ventilated
Use water integrated tools where possible
Check the equipment for signs of damage
Trainer to add contextual conclusions

## Slide 14
FURTHER LEARNING
Good Practices for Dry Cutting Applications Using Hand-Helf Angle Drinders/Cutters or Electric Wall Chasers (Task Sheet 2.1.14a)
Good Practices for Cutting and Polishing Ceramic and Stone Materials (Task Sheet 2.2.7)
NEPSI Good Practice Guide
NEPSI Guide for SMEs
Visit the NEPSI E-Learning Platform at training.nepsi.eu for more learning resources on RCS