## Slide 1
GOOD PRACTICES TRAINING FOR
SYSTEMS OF PACKAGING

## Slide 2
PREAMBLE (FOR TRAINER)
As part of the education step in implementing the NEPSI Good Practices, NEPSI has developed a set of educational resources.
Each PowerPoint Training pack covers a topic relevant for workers across all industries that use materials containing crystalline silica. The packs provide information about the dust exposure risks related to the topic and the good practices and measures available to reduce them. The purpose of the training is to inform and educate workers to help them to use the control measures effectively and reduce their exposure to respirable crystalline silica (RCS) in the workplace.
Use the blank template and placeholders to add additional information to this training pack as needed.

## Slide 3
PLEASE NOTE
The information in this PowerPoint training is advisory in nature and informational in content. It is not a standard or regulation, and it neither creates new legal obligations nor alters existing obligations created by health legislation and policy.

## Slide 4
INTRODUCTION
Learning to protect yourself against work-related hazards is a priority.
In this PowerPoint training, you will learn about:
How airborne dust may be generated in packing processes
How packaging systems are designed to minimise the release of airborne dust, including respirable crystalline silica dust (RCS)
What good practices you should follow to protect yourself from exposure to airborne dusts
Text for trainer to fill – if you’ve added a custom slide, insert a brief overview of the contextual material
Notes: Excessive exposure to respirable crystalline silica (RCS) can lead to serious health problems for workers in the long-term. For that reason, it is important that all workers are aware of the good practices that limit or eliminate exposure to silica dust”.
This training provides information about dust control in systems of packing. Keep in mind that a risk assessment is needed when designing a packing system, though this concerns primarily the management.

## Slide 5
DUST CONTROL TECHNIQUES
Dust created by systems of packing can be managed using enclosure, extraction/ventilation, PPE and good hygiene/housekeeping, which are four of the five main dust control techniques.
GOOD HYGIENE / HOUSEKEEPING
Washing work clothes and vacuuming up dust produced by processes stops dust accumulating over time – a clean workspace is a safe one
ENCLOSURE
Conducting RCS producing processes in a sealed environment prevents dust exposure at the source
EXTRACTION / VENTILATION
Capturing RCS at source, before we are exposed to it, and replacing contaminated air with clean air.
PROTECTIVE EQUIPMENT
PPE (e.g. Face masks) protects workers from dust when all other control measure are insufficient to control exposure risks
WATER
Keeping processes wet prevents dust becoming airborne by capturing particles with water

## Slide 6
THE RISKS FROM THIS ACTIVITY
This activity can be very dusty
Long term exposure to high levels of RCS can cause disabling lung disease
It’s important that we protect ourselves from exposure to this airborne dust every day.
By following good practices today, we protect our health for the future.
How will you spend your retirement?

## Slide 7
HOW PACKAGING SYSTEMS MAY GENERATE RCS
Packaging systems involve the handling of large quantities of material, which often contains crystalline silica.
The method of packing will influence the amount of airborne respirable dust that may be generated.
Dry materials tend to create more dust than moist materials
Faster, higher energy packing tends to create more dust
If compressed air is used to fluidise powdered material, more airborne dust may be released
More dust is generated when materials fall from a greater height

## Slide 8
REDUCING DUST EXPOSURE WITH PACKAGING SYSTEMS
The main dust control measures involve automation, enclosure of processes and ventilation
Automation helps to minimise workers’ contact with dusty processes, often allowing the work processes to be monitored remotely from a clean control room
Enclosure helps to minimise the spread of dust away from its source.
  A physical barrier between the process and the worker can achieve a high level of protection. However, precautions against exposure must be taken if needing to enter the enclosure!
  Ensuring a tight seal between filling nozzle and bag helps to prevent dust escaping
Exhaust ventilation captures the airborne dust at source, before we are exposed to it
Respiratory Protective Equipment may also be needed if the above controls are not sufficient.

## Slide 9
DOS AND DON’TS FOR SYSTEMS OF PACKAGING
DO
Use the dust control measures provided. Additionally, Respiratory Protective Equipment may be required.
Have a plan to deal with spills safely, and clean them up immediately using vacuum or wet cleaning methods
Ensure the ventilation systems are working effectively
Report defects to your supervisor
DON’T
Enter an enclosure without taking precautions against exposure, such as Respiratory Protective Equipment
Interfere with the control measures. They are provided for your safety and health.
Clean up with a dry brush. Use vacuum or wet cleaning instead.
Text for trainer – add additional information relevant to your work context

## Slide 10
CONCLUSION
The proper use of systems of packaging can help maintain a safe, dust-free working environment. Remember:
Always use the dust control measures provided
If you suspect the dust control measures are faulty, report this to the on-site manager.
Deal with spills immediately
Trainer to add contextual conclusions

## Slide 11
EMPTY SLIDE
Use this slide to create custom training material specific to a work environment/context.
To change the image, right click > change picture > from file.
To create more slides, click the ‘New Slide’ tab above.

## Slide 12
ADDITIONAL LEARNING MATERIALS
Good Practices for Systems of Packaging (Task Sheet 2.1.18)
NEPSI Good Practice Guide
NEPSI Guide for SMEs
Visit the NEPSI E-Learning Platform at training.nepsi.eu for more learning resources on RCS