## Slide 1
GOOD PRACTICES TRAINING FOR ENCLOSED HANDLING AND TRANSPORT SYSTEMS

## Slide 2
PREAMBLE (FOR TRAINER)
As part of the education step in implementing the NEPSI Good Practices, NEPSI has developed a set of educational resources.
Each PowerPoint Training pack covers a topic relevant for workers across all industries that use materials containing crystalline silica. The packs provide information about the dust exposure risks related to the topic and the good practices and measures available to reduce them. The purpose of the training is to inform and educate workers to help them to use the control measures effectively and reduce their exposure to respirable crystalline silica (RCS) in the workplace.
Use the blank template and placeholders to add additional information to this training pack as needed.

## Slide 3
PLEASE NOTE
The information in this PowerPoint training is advisory in nature and informational in content. It is not a standard or regulation, and it neither creates new legal obligations nor alters existing obligations created by health legislation and policy.

## Slide 4
INTRODUCTION
Learning to protect yourself against work-related hazards is a priority.
In this PowerPoint training, you will learn about:
How handling and transport systems are designed, fully enclosed, to prevent the release of respirable crystalline silica dust (RCS) into the workplace air as bulk materials are moved around
Text for trainer to fill – if you’ve added a custom slide, insert a brief overview of the contextual material
Notes: Excessive exposure to respirable crystalline silica (RCS) can lead to serious health problems for workers in the long-term. For that reason, it is important that all workers are aware of the good practices that limit or eliminate exposure to silica dust.
This training provides guidance on the different mechanical and pneumatic handling and transport systems for internal movement of crystalline silica containing products, and particularly those which are dry.

## Slide 5
DUST CONTROL TECHNIQUES
Handling and transport systems use enclosure to manage dust, which is one of the five main dust control techniques.
GOOD HYGIENE / HOUSEKEEPING
Washing work clothes and vacuuming up dust produced by processes stops dust accumulating over time – a clean workspace is a safe one
ENCLOSURE
Conducting RCS producing processes in a sealed environment prevents dust exposure at the source
EXTRACTION / VENTILATION
Capturing RCS at source, before we are exposed to it, and replacing contaminated air with clean air.
PROTECTIVE EQUIPMENT
PPE (e.g. Face masks) protects workers from dust when all other control measure are insufficient to control exposure risks
WATER
Keeping processes wet prevents dust becoming airborne by capturing particles with water

## Slide 6
THE RISKS FROM THIS ACTIVITY
The correct functioning of this equipment is essential to protect us against RCS.
Long term exposure to high levels of RCS can cause disabling lung disease
It’s important that we protect ourselves from exposure to this airborne dust every day.
By following good practices today, we protect our health for the future.
How will you spend your retirement?

## Slide 7
HOW ENCLOSED SYSTEMS HELP REDUCE EXPOSURE TO RCS
Enclosed systems are the most effective technical measures for dust control. The benefits include:
Reduced/eliminated dust exposure
Quick and cost-effective transportation of materials
Limited risk of human error and injury
Notes: Transporting materials containing crystalline silica can cause dust particles to become airborne. The most effective technical measure for dust control is to work in closed systems (encapsulation, enclosure).

## Slide 8
TYPES OF ENCLOSED TRANSPORT SYSTEMS
Screw conveyors
Conveyor belts
Bucket elevators
Vibratory feeds
Text for trainer — Add an image and information about transport systems specific to your work context (if applicable)
Notes: Transport systems are typically pneumatic (i.e. containing or operated by gas or air under pressure) as they are more efficient.
If an enclosed transport system isn’t available, the wetting of dry materials may be an alternative to full enclosure.

## Slide 9
DOS AND DON’TS OF ENCLOSED HANDLING SYSTEMS
DO
Check for visible signs of damage, especially at wear points (eg bends)
Clean up spills immediately using vacuum or wet cleaning methods
Check the condition of conveyor belt cleaning devices and adjust them as necessary
Inform the on-site supervisor of potential leakages/issues
Plan ahead for fault situations. For example, identify a safe way to clear blockages
DON’T
Overload the handling systems with materials
Transport objects that aren’t intended for the enclosed system
Make unauthorized changes to the system. Engage a competent specialist.

## Slide 10
EMPTY SLIDE
Use this slide to create custom training material specific to a work environment/context
To change the image, right click > change picture > from file
To create more slides, click the ‘New Slide’ tab above

## Slide 11
CONCLUSION
Enclosed transportation systems are the best way to control dust when bulk materials are in transit.
Remember:
Always use enclosed systems where available
Check the system for visible signs of damage
Report faults to your supervisor
Trainer to add contextual conclusions

## Slide 12
FURTHER LEARNING
Good Practices for Handling and Transport Systems (Task Sheet 2.1.11)
NEPSI Good Practice Guide
NEPSI Guide for SMEs
Visit the NEPSI E-Learning Platform at training.nepsi.eu for more learning resources on RCS