## Slide 1
GOOD PRACTICES TRAINING FOR
WET PROCESSES

## Slide 2
PREAMBLE (FOR TRAINER)
As part of the education step in implementing the NEPSI Good Practices, NEPSI has developed a set of educational resources.
Each PowerPoint Training pack covers a topic relevant for workers across all industries that use materials containing crystalline silica. The packs provide information about the dust exposure risks related to the topic and the good practices and measures available to reduce them. The purpose of the training is to inform and educate workers to help them to use the control measures effectively and reduce their exposure to respirable crystalline silica (RCS) in the workplace.
Use the blank template and placeholders to add additional information to this training pack as needed.

## Slide 3
PLEASE NOTE
The information in this PowerPoint training is advisory in nature and informational in content. It is not a standard or regulation, and it neither creates new legal obligations nor alters existing obligations created by health legislation and policy.

## Slide 4
INTRODUCTION
Learning to protect yourself against work-related hazards is a priority.
In this PowerPoint training, you will learn about:
How water is used in high-energy industrial processes to reduce exposure to respirable crystalline silica dust (RCS)
How and when to use wet processes
Best practices and dos & don’ts for wet processes
Text for trainer to fill – if you’ve added a custom slide, insert a brief overview of the contextual material
Notes: Excessive exposure to respirable crystalline silica (RCS) can lead to serious health problems for workers in the long-term. For that reason, it is important that all workers are aware of the good practices that limit or eliminate exposure to silica dust.
This training provides guidance for processing (e.g. drilling, cutting, sanding) materials containing crystalline silica using hand-held power tools with water system.

## Slide 5
DUST CONTROL TECHNIQUES
Wet processes is one of the five main dust control techniques.
GOOD HYGIENE / HOUSEKEEPING
Washing work clothes and vacuuming up dust produced by processes stops dust accumulating over time – a clean workspace is a safe one
ENCLOSURE
Conducting RCS producing processes in a sealed environment prevents dust exposure at the source
EXTRACTION / VENTILATION
Capturing RCS at source, before we are exposed to it, and replacing contaminated air with clean air.
PROTECTIVE EQUIPMENT
PPE (e.g. Face masks) protects workers from dust when all other control measure are insufficient to control exposure risks
WATER
Keeping processes wet prevents dust becoming airborne by capturing particles with water

## Slide 6
THE RISKS FROM THIS ACTIVITY
The correct functioning of this equipment is essential to protect us against RCS
Long term exposure to high levels of RCS can cause disabling lung disease
It’s important that we protect ourselves from exposure to this airborne dust every day.
By following good practices today, we protect our health for the future.
How will you spend your retirement?

## Slide 7
HOW WET PROCESSES REDUCE EXPOSURE TO RCS
Wet processes are used in high-energy industrial processes involving materials that contain crystalline silica, such as drilling, cutting, grinding and sanding. Water systems may be integrated into tools and equipment.
Water can be used to control airborne dust generated from vehicle movements on roads and construction sites, and also for general cleaning.
The water catches the dust particles stopping them from becoming airborne.
Notes: To avoid exposure to hazardous levels of dust generated by high-energy processes, keep processes wet. The use of water traps dust keeping exposure to a minimum.

## Slide 8
WATER ASSISTED DUST SUPPRESSION
Water reduces the levels of dust generated through high-energy processes.
(Click to play video.)
Notes: The following video shows the affect of water as a means of dust suppression in wet processes. Next to the video picture you see a graph and a red bar illustrating the dust concentration in mg/m3.
The measurement of the dust concentration is not about respirable crystalline silica, it is based on a semi-quantitative measurement. What is essential is not the dust concentration value but the relative difference between exposure levels during the recommended practice and other practice.

## Slide 9
USING WET PROCESSES
Wet processes are always preferred when available (and safe to use). When using wet processes:
Make sure the space is well ventilated
Make sure the water supply is appropriate and adequate for the task at hand
Clean up using wet methods
Protect water supplies against freezing
Check for bacterial growth caused by water sources, where airborne droplets may be formed
Notes: Wet processes should always be used when available to limit the generation of airborne dust. Not all power tools are adapted for wet process. Ensure that the equipment in use is appropriate for the task at hand.
Before using wet processes, ensure that the equipment and water system are working correctly. If you suspect the equipment isn’t functioning properly, contact the on-site manager.

## Slide 10
DOS AND DON’TS FOR WET PROCESSES
DO
Use water assisted dust suppression when it is possible and safe to do so
Ensure that water is disposed of to an appropriate drainage system
Clean up spills and puddles immediately
DON’T
Use excessive water pressure that can disturb settled dust. A fine mist or spray is more effective than a jet.
Use water assisted suppression on devices that don’t support water infiltration
Text for trainer — Add additional text about measures related to wet processes relevant to your own context

## Slide 11
EMPTY SLIDE
Use this slide to create custom training material specific to a work environment/context
To change the image, right click > change picture > from file
To create more slides, click the ‘New Slide’ tab above

## Slide 12
CONCLUSION
Wet processes keep dust to a minimum and reduce the risk of RCS exposure.
Remember:
Always use water systems when available
Ensure water systems are appropriate and adequate for the task at hand
If you suspect a water system isn’t working correctly, contact the on-site manager

## Slide 13
FURTHER LEARNING
Good Practices for Wet Processing of Mineral Workpieces Containing Crystallin Silica Using Hand-Held Power Tools (Task Sheet 2.1.14d)
Good Practices for Using Water/Additives on the Roads or Open Surfaces to Reduce Dust Levels (Task Sheet 2.2.27)
Good Practices for Water Assisted Dust Supression (Task Sheet 2.2.35)
Good Practices for Wet Cutting Processes of Masonry Units, Agglomerated and Natural Stones (Task Sheet 2.2.42)
NEPSI Good Practice Guide
NEPSI Guide for SMEs
Visit the NEPSI E-Learning Platform at training.nepsi.eu for more learning resources on RCS